Vibrio vulnificus

| MINIMUM PERSONAL PROTECTIVE EQUIPMENT |
| --- |
| Minimum Requirements See Section 4.6 of UBM for details | Tie back hair and wear closed-toe shoes, street clothing fully covering legs, lab coat, disposable gloves. Additional requirements listed in Section 15 of your lab-specific biosafety manual must be followed. |
| Additional Precautions | If centrifuge is outside of BSC and rotors are not sealed, wait 5 minutes after centrifuge completely stops before opening centrifuge. |

| VIABILITY |
| --- |
| Disinfection | Use 10 % Bleach for 20-30 minutes or acceptable time approved by IBC and EHS; or 70 % ethanol (spread over area and allow surface to air dry). |
| Physical inactivation | Autoclave and dispose of as Regulated Medical Waste (RMW). See waste information for disposal of solid and liquid waste. |
| Survival Outside of Host | Survives well in water, and in warm temperatures. |

| MEDICAL-RELATED INFORMATION |
| --- |
| Prophylaxis availability | None |
| Vaccine availability | None |
| Medical Information | You should inform the physician of any drug resistance(s) acquired by the lab strain(s) and any sequences inserted into the lab strain(s). |
| Surveillance | Monitor for symptoms of infection (see “Health Hazards”) |
| VT Requirements | Immediately report any exposures to Occupational Health. |

| REFERENCES & SOURCES |
| --- |
| Montana State University; Biosafety Program | http://www.montana.edu/orc/biosafety/index.html |
| Canadian PSDS and Risk Assessment | http://www.phac-aspc.gc.ca/lab-bio/res/psds-ftss/index-eng.php |
| BMBL; 5th Edition | http://www.cdc.gov/biosafety/publications/bmbl5/BM BL.pdf |
| CDC | https://www.cdc.gov/ |
| NIH Guidelines | https://osp.od.nih.gov/biotechnology/nih-guidelines/ |

| CONTAINMENT REQUIREMENTS and NOTES |
| --- |
| BSL-2 | All procedures must be performed in a BSC, unless otherwise approved and stated in lab-specific manual. |
| ABSL2 | For all procedures utilizing infected animals. |
| ACL2 | For all procedures utilizing infected arthropods. |
| BL2/BLN-2/BLP-2 | Follow all applicable NIH Guideline requirements. |
| RG2 | Agents that are associated with human disease which is rarely serious and for which preventive or therapeutic interventions are often available. |

| AGENT CHARACTERISTICS |
| --- |
| Morphology | Gram-negative, facultative anaerobe, halophilic, non-spore forming, curved, rod-shaped bacterium. |
| Zoonosis | Yes, oysters |
| Diseases | Vibriosis, skin infection, septicemia |

| SPILL INFORMATION |
| --- |
| Small (Refer to Section 3 of the LSBM for details on clean-up) | Notify others working in the lab. If contaminated, remove PPE and do new PPE. Follow spill procedures in Section 3 of the Lab-specific Biosafety Manual. |
| Large (Refer to Section 1.8 of the UBM for details on spill clean-up) | Immediately notify all personnel in the lab and clear all personnel from the area. Remove any contaminated PPE/clothing and leave the lab. Secure the area by locking doors, posting signage and guarding the area to keep people out of the space. Call 911 or non-emergency Campus Police (231-6411) and ask to notify EHS. Inform the PI or Lab Manager/ Supervisor as soon as possible. |

| HEALTH HAZARDS |
| --- |
| Host Range | Humans and seafood |
| Modes of Transmission in Lab | Accidental ingestion, accidental puncture of skin, exposure of mucous membranes. |
| Signs and Symptoms | Redness and swelling at area of exposure, watery diarrhea, abdominal cramping, nausea, vomiting, fever, chills. |
| Infectious Dose | Best estimate, 102 – 10-9 CFU, maybe less than 102 CFU |
| Incubation Period | 16 hours – several days, 4 hours in wound infections |

| EXPOSURE INFORMATION |
| --- |
| Eyes and Mucous membranes (See Section 1.3 and 1.5 of UBM for specific details) | Eyes: Flush eyes for 5-10 minutes at eyewash station. Immediately flush membranes with plain water. Go to an appropriate healthcare provider for treatment. Inform the health care provider of the biohazardous material(s) to which you have been exposed and bring risk assessments/ SDSs. |
| Needle Sticks and open wounds (See Section 1.4 of UBM for details) | Clean and wash area thoroughly, using soap and water for a minimum of 5 minutes. If a needlestick, gently massage the area to make it bleed while washing. Go to an appropriate healthcare provider for treatment. Inform the health care provider of the biohazardous material(s) to which you have been exposed and bring risk assessments/ SDSs. |

| LABORATORY HAZARDS |
| --- |
| Laboratory Acquired Infections (LAIs) | Some cases have been reported. |
| Sources | Cultures, frozen stocks, other samples described in IBC protocol. |

| WASTE INFORMATION |
| --- |
| Waste Disposal | Refer to the EHS Laboratory Waste Charts for details on disposal of biohazardous waste. |

| LAB-SPECIFIC INFORMATION: Check the response that is applicable to your lab |
| --- |
|  | I have reviewed the above information and my lab will follow all requirements as described above. |
|  | I have reviewed the above information and my lab will follow all requirements as described above with the following changes specific to my lab: |